## Slide 1
e(i)
Optimized method
Set autoregulation measure IAR IAR = 0 for normocapnia (‘good autoregulation’) IAR = 1 for hypercapnia (‘poor autoregulation’)
Regress filter parameters against IAR IAR = c(0).h(0) + c(1).h(1) + … + c(6).h(6) +e where c(k) are weights and e is the residual error
An estimated impulse and step response
Methods
27 healthy adult volunteers (18-55 years), at rest.
Normo- and hypercapnia (beathing 5% CO2 in air)
Simultaneously record
  Cerebral blood flow velocity (CBFV) via Transcranial Doppler in middle cerebral artery
  Arterial blood pressure (ABP ) via Finometer
  Normalize CBFV and ABP  % change
A segment of one recording
Quantifying autoregulation from estimated model parameters: an optimization approach
David M. Simpson1, Claudio Henriques Berroeta2, Emmanuel Katsogridakis3, Ronney B. Panerai3
1 ISVR/FEE, University of Southampton, SO17 1BJ, UK, ds@isvr.soton.ac.uk
2 Department of Computing, Central University, Santiago de Chile, Chile
3Department of Cardiovascular Sciences, University of Leicester, UK, rp9@leicester.ac.uk
Abstract: In order to quantify cerebral autoregulation (CA), one of the most commonly used techniques is to fit a linear model to the recorded signals, with arterial blood pressure (ABP) as input and cerebral blood flow velocity (CBFV) as output. Then parameters are extracted from the model to quantify CA: for example average phase or gain in a narrow frequency band, or features of the predicted step-response. We propose an optimized method to distinguish between CA during normocapnia and hypercapnia. In 27 adults (18-55 years old) at rest, CBFV and ABP were recorded simultaneously during normocapnia and then hypercapnia induced by breathing 5% CO2 in air. Recordings were repeated on a separate day, giving a total of 108 recordings of approximately 5 minutes each, each resampled at 1 Hz. The interrelationship between ABP and CBFV was modelled using a linear finite-impulse-response filter (7 coefficients). Multiple linear regression of these coefficients was used to predict normocapnia (1) or hypercapnia (0), achieving an area under the ROC curve of 0.91, considerably better than ARI (0.81) and slightly higher than for phase-lead at 0.1 Hz (0.88). The method provides a new, data-driven and optimized parameter for assessing autoregulation. This work is being extended to include non-linear classifiers (support vector machines).
Background
Cerebral autoregulation: mechanism that keeps blood flow to the brain approximately constant when blood pressure changes
Can be quantified from dynamic response estimated from simultaneous recordings of blood flow and pressure
Commonly a mathematical model is fitted between the input signal (arterial blood pressure) and the output (cerebral blood flow velocity). Autoregulation is then quantified by extracting some index from the model (e.g. phase or gain at 0.1 Hz)
Which parameter is ‘best’ remains an open problem.
Objectives
What is the ‘optimal’ index to distinguish between autoregulation in normo- and hypercapnia?
-
+
p(i)
v(i)
h(i)
Model input-output system with an FIR filter
  v(i)=h(0)p(i)+h(1)p(i-1)+ … + h(6)p(i-6) + e(i), where i is sample index, v is CBFV p is ABP and h is the impulse response
Results
Regression coefficients
Linear regression shows weighting to ‘best’ distinguish between normo- and hypercapnia.
Bootstrap tests show good consistency in results.
Discussion and Conclusions
Optimized method leads to improved prediction of experimental condition (area under the ROC curve)
Further statistical analysis (e.g. cross-validation) is required to remove bias in performance measure
The weights (c(k)) can be interpreted as the (time-reversed) optimal input.
The use of hypercapnia as a proxy for impaired autoregulation is open to question.
The method presented can be used with alternative outcome measures (e.g. clinical outcome).
The method provides an optimized link between mathematical modelling and clinical inference.
estimated
v(i)
Minimize e(i)
V(f)=H(f).P(f)+E(f)  H(f)=|H(f)|e-j(f)
Estimate autoregulation from
  Phase at 0.1 Hz
  ARI (from best-fit Tiecks’ model)
  Optimized method
In the absence of a gold-standard measure for autoregulation, hypercapnia is often used to provoke impairment.
ROC curves for autoregulation measures
Optimized method gives highest area under ROC curve
Nonlinear methods (e.g. neural networks) did not yield major improvements
Area under the ROC curve
Optimized: 0.91
ARI: 0.81
Phase: 0.88
Acknowledgement:

## Slide 2
0
0.2
0.4
0.6
0.8
1
0
0.2
0.4
0.6
0.8
1
1-Specificity
Sensitivity